## Slide 1: aiPiCar DGMD FALL 2019 PROJECT
Building a Self-Driving Raspberry Pi Car Capable of Lane Following, Object Recognitions and Obstacle Avoidance
Project By: Alex Andony
https://github.com/ando11235/aiPiCar

## Slide 2: Project Overview
The goal of this project is to demonstrate self-driving autonomous technological concepts using a small Robotic Car powered by a Raspberry Pi, at a price tag under $400.
  Assemble the PiCar Kit and Base Raspberry Pi Operating System
  Demonstrate Autonomous “Lane Following” through OpenCV
  Demonstrate Advanced Camera recognition features, including adapting to street signs and basic obstacle avoidance
  Put everything together, demonstrating a real world application scenario involving both lane following and object recognition

## Slide 3: aiPiCar: hardware
Car Kit Used: SunFounder Smart Car Kit
CPU: Raspberry Pi 3 B+ (B Plus) Rasbpian Buster v. Sept 2019
Wide Angle Camera Upgrade: WLP Wide Angle USB Camera
CPU Upgrade: Coral EdgeTPU USB Accelerator
Laptop: Apple Macbook Pro Catalina v10.15.1

## Slide 4: Initial Setup Challenges
New to Raspberry Pi Development
New Raspbian Version released recently (Buster)
Compatibilities with Buster, Python, OpenCV, Edge TPU
aiPiCar running via remote control

## Slide 5: Lane Detection and Self Driving: OpenCV
Display Raw Video Stream
Apply HSV Color Filter
Apply Blue Color Mask
Detect Edges of Mask with Canny
Isolate Region of Interest (Lower Half of Image)
Detect Line Segments Using Hough Transform and Overlay Original Video

## Slide 6
aiPiCar lane recognition with OpenCV

## Slide 7: Sign Recognition and Obstacle Avoidance
Model Training:
  Transfer Learning
  MobileNet v2 SSD COCO Quantized
  Image Capture and Labeling
  Training with Collab Notebook
  Conversion of Model to TensorFlow Lite flatbuffer file (Google Edge)

## Slide 8
aiPiCar person detection
aiPiCar stop sign detection
aiPiCar speed limit detection

## Slide 9: Aipicar Practical Demonstration: School Zone
Lane Following
Slow Down (25 mph sign recognition)
Stop for Pedestrian
Stop at Stop Sign
Speed Up (40 mph sign recognition)
AGH! Another Pedestrian!

## Slide 10: Lessons Learned and Opportunities for Future Teams
RaspberryPi, macOS, EdgeTPU
Advanced Lane Following using Machine Learning
  Current Model: OpenCV
  Problems: Extremely sensitive (blue, lighting, noise)
  Training Model based approach
Advanced Object Detection using End-to-End Machine Learning Approach
  NVIDEA Paper Model: CNN training
  Feed “Good Driver” Behavior Videos